## Slide 1
TECHNOLOGY DEVELOPMENT PROPOSAL · FTBI–TEXMiN MINING CPS CoE
Underground Audio/Video
Communication System
for Miner Safety
and Monitoring
Hybrid free-space optical and LoRa communication for real-time video and emergency alerts in underground mines.
50–100 m
50–100 m
Focus
4S Mining
Safe, Smart, Sustainable, Social
Funding
₹15 lakh
24 months
Readiness
TRL 2 → TRL 5
Tunnel-level validation
Institute
NIT Rourkela
Prof. Sadananda Behera, PI
Prof. Sadananda Behera, Assistant Professor · 98610 77539 · No co-PI · Industry letter: not attached
NIT Rourkela · FTBI–TEXMiN · Title
1 / 15
Notes: Open with the problem in one sentence, then the frame.
Underground mines lose the link to the surface when it is most needed. This proposal builds a hybrid link: real-time video on a free-space optical hop of 50 to 100 metres, and a LoRa path for control and alerts when that hop is down.
State the frame: NIT Rourkela, 4S Mining, 15 lakh, 24 months, TRL 2 to TRL 5. Say that an industry letter is not attached; the plan for it is a later slide. A working auto-tracking FSO prototype already exists in the department and will be used.

## Slide 2
01 · PROJECT TITLE AND OBJECTIVES
Objective
NIT Rourkela · FTBI–TEXMiN · Objectives
2 / 15
Real-time video from a mine heading to the surface on aligned free-space optical hops, with LoRa keeping the alert path alive.
Specific objectives
1
50–100 m
Real-time video on FSO links between successive tunnel nodes
2
IMU
Auto-tracking with motorized steering. Department prototype already working
3
LoRa
Control, alerts and fallback when an optical hop is interrupted
4
Multi-hop
Transmitter, relays, surface base station. Lab and tunnel-like tests
Notes: Read the objective once. Then the four points, without adding claims.
Point 2 is the one to pause on: alignment is not a new start. The department already has a working auto-tracking FSO prototype. This grant puts video on it, adds LoRa, and makes it a mine node.
Point 4 is the limit of the grant: laboratory plus a tunnel-like or underground test. A production-mine product trial comes after.

## Slide 3
02 · PROBLEM STATEMENT AND RELEVANCE TO THE MINING SECTOR
Background: communication underground today
NIT Rourkela · FTBI–TEXMiN · Background and problem
3 / 15
Miners at the face depend on a link that rock, water and ground movement regularly remove.
Surface control room
✕
Wi-Fi, LTE: no signal in rock
Cable cut by fall, water, machines
Voice and text do not show the face
What mines use now
Wired phones
Leaky-feeder cable
Low-rate radio
Surface control room
Need: video where there is line of sight, and an alert that survives a cut cable.
Notes: This is the background from the earlier deck, stated plainly.
Present practice is leaky feeder and wired phones, plus low-rate radio. It is enough for voice on a drift that is still intact. It is not enough when the cable goes with the fall, and it never shows the face.
DGMS: do not promise certification in this grant. Say that dependable communication is part of mine safety practice, and that any statutory clearance will be taken before production deployment, as written in the proposal.
If asked what changed since the earlier presentation: the problem is the same. The system in the submitted proposal is the hybrid FSO–LoRa relay, built on the auto-tracking hardware already in the department. A handheld RFID device is not the deliverable of this grant.

## Slide 4
02 · PROBLEM STATEMENT AND RELEVANCE TO THE MINING SECTOR
Relevance to underground mining
NIT Rourkela · FTBI–TEXMiN · Relevance to mining
4 / 15
What an underground heading needs, set against the systems available today.
Cable / leaky feeder
Wi-Fi / LTE
LoRa only
FSO only
This proposal
Reach the surface in an emergency
~
Until the cable is cut
✕
No signal in rock
✓
Yes, at low data rate
~
Only with clear sightline
✓
LoRa stays up if beam drops
Live picture of the face
✕
Not what it is for
✕
No usable bandwidth
✕
Too slow for video
✓
Yes, while aligned
✓
Aligned by closed loop
After vibration or a fall
✕
Cable often fails too
✕
Link lost
✓
Alert can still be sent
✕
Beam is lost
✓
Alert stays. Beam reacquired
Fit for an Indian underground mine
~
Often imported
✕
Not an underground system
~
Sensors, not video
~
Mostly shown in lab
✓
Indigenous node
Works
Partly
Does not
Safe
Picture of the face, alert if it drops
Smart
Camera, IMU, radios and steering in one node
Sustainable
Heavy data on light, control on low-power radio
Social
Fewer people sent into a heading unseen
Notes: Stay on the last column. Cable reaches the surface until it is cut. LoRa can carry the alert and cannot carry the video. FSO can carry the video and loses it when the mount moves. This proposal keeps both, on a hop the length of a straight stretch of tunnel.
Do not claim this replaces leaky feeder for voice across a whole mine. It is a heading kit: video on the clear spans, an alert that does not share the fate of the cable.
4S is the focus area ticked in the proposal. One clause each is enough.

## Slide 5
03 · INNOVATION AND UNIQUENESS
What is different in the proposed system
NIT Rourkela · FTBI–TEXMiN · Innovation
5 / 15
1
Hybrid FSO and LoRa
FSO carries video. LoRa carries control, alerts and backup.
2
Multi-hop along the tunnel
A node every 50–100 m on line of sight. A longer heading means more relays, not a stronger laser.
3
IMU auto-tracking
IMU drives a motorized mount and corrects pointing. Prototype exists in the department.
4
Video as safety
A live view of the zone a team is about to enter.
5
One cyber-physical node
Senses (camera, IMU, gas, temperature, humidity), communicates, and steers the beam.
Why FSO works underground
Open tunnel, not rock
Notes: Spend time on points 2 and 3. Those answer the objection that FSO cannot work underground.
Point 2: the link is along the open tunnel, 50 to 100 metres, then repeated. Point 3: the mount is part of the link, and the first version of it already runs in the department.
Point 1 is the architecture in the proposal figure. Point 4 is the mining use of the bandwidth. Point 5 is why the work belongs in a CPS centre.
Import, if there is time: mine communication systems of this class are largely bought from Germany, the USA and China. This is an indigenous design for the tunnel in front of us.

## Slide 6
04 · TECHNICAL FEASIBILITY AND METHODOLOGY
Proposed scheme
NIT Rourkela · FTBI–TEXMiN · Proposed scheme
6 / 15
Surface base station
50–100 m
50–100 m
50–100 m
Transmitter node
Relay node
Relay node
Last relay
FSO link: real-time video
LoRa link: control, alerts, backup
Each node
Laser · IMU · motorized mount · LoRa
Surface
Dashboard · alerts · localization
Notes: Leave this figure up. Walk it left to right.
Each underground node has four parts: FSO laser, IMU, motorized alignment, LoRa. The optical beam between two nodes is the video path, 50 to 100 metres, steered by the IMU. The chain continues to transceiver n. The surface station receives the monitoring view and the LoRa alerts.
If a span is blocked or the beam walks off, the video on that span stops and the LoRa alert does not. The tracking loop then tries to reacquire.
Do not invent a bitrate or a latency. Those targets are fixed in the first three months, after the camera and the laser are selected.

## Slide 7
04 · TECHNICAL FEASIBILITY AND METHODOLOGY
How one hop works
NIT Rourkela · FTBI–TEXMiN · How one hop works
7 / 15
The picture travels only on light. Each node rebuilds it, checks it, and sends it on.
Optical frame
AA55
Length
Seq
JPEG
CRC-16
UART 115200 8N1, one direction
Camera node
• Camera + Raspberry Pi
• Packet out of UART
• 650 nm laser, on–off keying
light
Relay node
• Photodiode, amplifier, comparator
• Second Pi checks CRC, holds JPEG
• Sends the frame again on its own laser
light
Base station
• Same receiver chain
• Third Pi checks CRC
• JPEG on the HDMI screen
Three different jobs
1
Laser
Carries the JPEG, and nothing else.
2
IMU
Holds the camera head at its angle. It does not find the relay.
3
LoRa
Five bytes: lock or lost, alert, image OK. No JPEG.
Notes: Walk the three boxes left to right. The camera node wraps one JPEG in a small frame and keys the laser with it. The relay does not amplify light: it rebuilds the frame, checks the CRC and transmits it again, so an error does not travel further. The base shows the JPEG on the screen. If the picture is on the screen, both hops worked.
Three jobs, three channels. Laser: JPEG only. IMU: holds the angle of the camera head, it cannot see the relay or the beam. LoRa: five bytes, LOCK or LOST from the relay, ALERT or IMG_OK to the base. If either laser is blocked the screen goes blank and the alert still arrives.

## Slide 8
04 · TECHNICAL FEASIBILITY AND METHODOLOGY
Starting point: auto-tracking FSO already working
NIT Rourkela · FTBI–TEXMiN · Feasibility
8 / 15
Auto-tracking FSO prototype, department lab. It will be used, not rebuilt.
What this grant adds
+
Video on the optical hop
+
LoRa for alerts and fallback
+
Relay nodes along a heading
+
Surface station, underground enclosure
Why it can be built here
50–100 m
hop within ordinary laser and photodiode modules
In the lab
FSO transceivers, embedded benches, computing
Designed loss
beam drops, alert goes on LoRa
First milestone: laboratory bench, one relay
Relay laser hand-aimed. IMU loop off for the first JPEG.
Camera node
existing gimbal + camera, Pi, laser
2–5 m
Relay
the one new node
2–5 m
Base
receiver, Pi, HDMI screen
Notes: Show the photograph. Say clearly: this is a working auto-tracking FSO system in the department, and the project will use it.
Do not quote a range or an accuracy for this unit unless you have the measured number in front of you. The design target for the mine hop, 50 to 100 metres, is the proposal target, not a result already claimed for this bench unit.
Then the four additions: video, LoRa, relays, underground enclosure and trial. The feasibility points are physics and facilities, not adjectives.
The bench strip at the bottom is the first milestone: one camera node, the one new relay node, and a base, 2 to 5 metres apart. One JPEG is sent hop by hop. If the picture appears on the base screen, both hops work and the tracking loop can be switched on.

## Slide 9
04 · TECHNICAL FEASIBILITY AND METHODOLOGY
Work plan — 24 months
NIT Rourkela · FTBI–TEXMiN · Work plan
9 / 15
Year 1
Year 2
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
1
Procure FSO, IMU, LoRa, cameras, mounts
2
Architecture and communication framework
3
Auto-tracking on the mine node
4
Integrate transmitter, relays, base
5
Laboratory tests
6
Tunnel-like / underground test
7
Documentation, patent, commercial plan
Milestones: M3 hardware · M7 architecture · M11 tracking · M16 integrated · M19 lab · M22 field · M24 report
Risk management
Technical
LoRa backup and modular hardware
Operational
Phased build with test checkpoints
Financial
Conservative budget margins
Notes: Do not read every row. Give the gates: month 3 hardware, month 7 architecture, month 11 tracker, month 16 integrated prototype, month 19 laboratory, month 22 tunnel-like test, month 24 patent and commercialization plan.
Point at months 8 to 11 and say that this block adapts the prototype already running in the department. The dates in the proposal are unchanged.
The tunnel trial does not start unless the month 16 and month 19 results justify it. If the optical hop drops during the trial, LoRa is the path under test for the alert.

## Slide 10
05 · EXPECTED OUTCOMES AND TECHNOLOGY READINESS LEVEL
Outcomes and readiness
NIT Rourkela · FTBI–TEXMiN · Outcomes and TRL
10 / 15
Readiness
TRL 1
TRL 2
TRL 3
TRL 4
TRL 5
TRL 6
TRL 7
TRL 8
TRL 9
Today
integrated system
Month 24
tunnel-like test
After this grant
needs a test mine
Deliverables
1
Hybrid FSO–LoRa prototype: transmitter, relays, surface base station
2
Real-time video over more than one optical hop
3
Auto-tracking recovering from deliberate misalignment
4
LoRa alert delivered when a hop is interrupted
5
Validation report, deployment guidelines, commercialization plan, patent filing
Notes: Be exact on the numbers. Do not raise the integrated system above TRL 2. The proposal says TRL 2. What is ahead of that is the auto-tracking prototype, which is a subsystem, not the whole mine link.
Month 24 commitment is TRL 5: relevant environment, meaning tunnel-like or underground, not only the optical bench. TRL 6 needs a partner or TEXMiN site and is outside this budget.
If they ask for numbers we will measure, and not for numbers we already have: hop length against 50–100 m, video continuity, time to realign, whether the alert arrives when the beam is blocked, and energy per node. Latency and bitrate are set in months 1 to 3.

## Slide 11
06 · INDUSTRY READINESS AND COLLABORATION
Industry engagement
NIT Rourkela · FTBI–TEXMiN · Industry
11 / 15
No industry letter is attached. It is to be earned from an operator or manufacturer who has seen a supervised trial.
1
Months 1–6
Find partners
Identify an underground operator and a mine-communications maker with TEXMiN and the industry cell. Ask for a letter of interest.
2
Months 6–12
Workshop
Their engineer on mounting, power, dust, gas zones. Constraints frozen before the enclosure closes.
3
Months 18–22
Trial
TEXMiN test mine or partner drift, engineer present. Report video, realignment, alert delivery.
4
Months 22–24
Next step
Licence or pilot talk. FTBI incubation if it becomes a venture.
Users
Underground coal and metal mines (managers, safety officers, rescue rooms) and mine-communication equipment makers.
Asked of TEXMiN, non-financial
Mentorship on mining standards, commercialization guidance, and test-mine access if it can be arranged.
Notes: Say the first sentence before anyone asks. A letter is not in the file.
Do not name Coal India or any other company as a partner. They are the class of user.
The useful introduction from the committee is a safety or communications engineer who will spend time on constraints in months 6 to 12, before the mechanical design is frozen.
Regulatory clearance is taken before product deployment, as the proposal states, not before the laboratory work.

## Slide 12
07 · IMPACT AND COMMERCIALIZATION PLAN
Impact, and how it would be deployed
NIT Rourkela · FTBI–TEXMiN · Impact and commercialization
12 / 15
What the tunnel trial will measure
Video continuity
on a 50–100 m hop
Alert delivery
when the hop is interrupted
Realignment time
after a deliberate disturbance
Energy per node
and bill of materials
What it changes for a mine
1
Re-entry decisions taken with a current picture of the face
2
The alert does not depend on a single cable
3
An indigenous node, where this class is largely imported
Commercial path
This grant
Proves one heading
Pilot
Supervised, with the partner who signs the letter
Licence or FTBI
Manufacturer licence, or incubated venture
Scale
Coverage grows by adding hops
Also fits
Tunnel monitoring
Underground transport
Oil and gas sites
Notes: The left side of the argument is the four measurements. Read one of them: when the beam is blocked, does the alert still arrive?
Do not quote lives saved, downtime percentages or rupees. We do not have those figures. The trial is how they would be obtained.
Commercial unit is a heading: node, relays, surface station. That is why a 15 lakh prototype is a step toward a product.
Later extensions, only if asked: video analytics, gas-trend monitoring, robotic nodes. They are in the proposal as future work. They are not month-24 deliverables.

## Slide 13
08 · TEAM DETAILS AND BUDGET SUMMARY
Team
NIT Rourkela · FTBI–TEXMiN · Team
13 / 15
Principal Investigator
Prof. Sadananda Behera
Assistant Professor
NIT Rourkela
98610 77539
No co-PI. Two project assistants for 24 months. The PI leads every work package.
Mining practice comes from TEXMiN mentors and the industry engineer, before the enclosure is frozen.
Relevant experience
JLT, JOCN
Optical links under impairment: soft-failure detection and localization
Indian patent
Published application for a deployable hardware testbed
2 DoT / TCoE projects
Co-PI on 6G projects, about ₹80 lakh and ₹82.4 lakh. One is a hybrid transceiver
Division of the work
Project assistant 1
Hardware: FSO, IMU, pan-tilt, LoRa, PCB, enclosure
₹15,000 / month
Project assistant 2
Software: multi-hop forwarding, video, tracking loop, surface display
₹15,000 / month
Notes: One line of credibility: the PI’s work is optical links under impairment, and hardware that leaves the simulator. This project points that at a mine heading.
Do not read the publication list. If asked: JLT and JOCN; Indian patent application 202631017889, published 2026; two ongoing DoT projects, of which the hybrid transceiver is the closest.
The question to expect: there is no mining co-PI. Answer from the third bullet. Mining constraints enter through TEXMiN and the industry workshop. This group builds the link.

## Slide 14
08 · TEAM DETAILS AND BUDGET SUMMARY
Budget — ₹15.00 lakh
NIT Rourkela · FTBI–TEXMiN · Budget
14 / 15
In ₹ lakh. Institute overhead is zero. Year 1 is ₹7.60 lakh and Year 2 is ₹7.40 lakh.
Chart: 
| Project assistants | Equipment | Consumables | Contingency | Travel
Budget | 7.2 | 3.5 | 1.5 | 1.5 | 1.3
₹15.00
lakh · 24 months
Head | Year 1 | Year 2 | Total | Share
Project assistants (2) | 3.60 | 3.60 | 7.20 | 48%
Equipment | 2.00 | 1.50 | 3.50 | 23%
Consumables | 0.75 | 0.75 | 1.50 | 10%
Contingency | 0.75 | 0.75 | 1.50 | 10%
Travel | 0.50 | 0.80 | 1.30 | 9%
Overhead | 0 | 0 | 0 | 0%
Total | 7.60 | 7.40 | 15.00 | 100%
Equipment
Year 1: FSO modules, pan-tilt, IMUs, controllers, cameras, LoRa and gateway, batteries, enclosures, edge computer, optics. Year 2: LoRa antennas, PCB fabrication, 3D printer for mounts.
Notes: One sentence: fifteen lakh, no overhead, two people and the hardware for one heading.
The columns add up: 7.20 + 3.50 + 1.50 + 1.50 + 1.30 = 15.00. Year split 7.60 and 7.40.
Salary is the largest head because the work is a build. Two assistants at 15,000 rupees a month for 24 months is 7.20 lakh. Equipment stays at 3.50 lakh because the unit under test is a heading, not a mine-wide installation. Travel is higher in year 2 because that is the tunnel trial.
Gas, temperature and humidity sensors are in the proposal justification and sit inside the hardware and consumables.

## Slide 15
FTBI–TEXMiN MINING CPS CoE
Thank you.
Request: ₹15 lakh over 24 months, to take the department’s auto-tracking FSO prototype to a hybrid underground link, validated at TRL 5.
Prof. Sadananda Behera
Assistant Professor, National Institute of Technology Rourkela
98610 77539
NIT Rourkela · FTBI–TEXMiN · Close
15 / 15
Notes: Read the request once and stop. Invite questions.
Answers to keep short:
Letter — not in the file. Months 1–6 find the counterpart, 6–12 learn their heading, 18–22 trial with them present.
Why FSO underground — the beam crosses open tunnel, 50–100 m, not rock. Relays follow the heading. The IMU mount exists because a fixed bracket will not hold, and a version of it already runs in the department.
Leaky feeder — remains useful for voice on an equipped drift. This work adds a picture and an alert path on one heading.
TRL — integrated system is TRL 2. Auto-tracking prototype is already working. Target is TRL 5. TRL 6 needs a partner site.
No mining co-PI — TEXMiN mentors and the month-6 workshop. The enclosure is not frozen before that.
Audio — the new capacity is live video. LoRa carries alerts and control.
Laser safety — power, enclosure and exposure are part of the month-6 constraints. Clearance before any production deployment.