## Slide 1
TECHNOLOGY DEVELOPMENT PROPOSAL · FTBI–TEXMiN MINING CPS CoE
Underground Audio/Video
Communication System
for Miner Safety and Monitoring
Hybrid free-space optical and LoRa communication for real-time video
and emergency alerts in underground mines.
Focus
4S Mining
Safe, Smart, Sustainable, Social
Funding
₹15 lakh
24 months
Readiness
TRL 2 → TRL 5
Tunnel-level validation
Institute
NIT Rourkela
Prof. Sadananda Behera, PI
Prof. Sadananda Behera, Assistant Professor
98610 77539 · No co-PI · Industry letter: not attached
NIT Rourkela · FTBI–TEXMiN · Title
1 / 14
Notes: Open with the problem in one sentence, then the frame.
Underground mines lose the link to the surface when it is most needed. This proposal builds a hybrid link: real-time video on a free-space optical hop of 50 to 100 metres, and a LoRa path for control and alerts when that hop is down.
State the frame: NIT Rourkela, 4S Mining, 15 lakh, 24 months, TRL 2 to TRL 5. Say that an industry letter is not attached; the plan for it is a later slide. A working auto-tracking FSO prototype already exists in the department and will be used.

## Slide 2
01 · PROJECT TITLE AND OBJECTIVES
Objective
NIT Rourkela · FTBI–TEXMiN · Objectives
2 / 14
Real-time video from a mine heading to the surface, on aligned free-space optical hops, with LoRa keeping the alert path alive.
Specific objectives
1
50–100 m
Video on FSO hops between successive tunnel nodes
2
IMU
Auto-tracking loop with motorized steering. Department prototype already working
3
LoRa
Control, alerts and fallback when a hop is interrupted
4
Multi-hop
Transmitter, relays and surface base station, tested in lab and tunnel-like setting
Notes: Read the objective once. Then the four points, without adding claims.
Point 2 is the one to pause on: alignment is not a new start. The department already has a working auto-tracking FSO prototype. This grant puts video on it, adds LoRa, and makes it a mine node.
Point 4 is the limit of the grant: laboratory plus a tunnel-like or underground test. A production-mine product trial comes after.

## Slide 3
02 · PROBLEM STATEMENT AND RELEVANCE TO THE MINING SECTOR
Background: communication underground today
NIT Rourkela · FTBI–TEXMiN · Background and problem
3 / 14
Miners at the face depend on a link that rock, water and ground movement regularly remove.
What mines use now
• Wired phones and leaky-feeder cable
• Low-rate radio for voice and short messages
• Surface control room for routine work and rescue
Where it fails
• Wi-Fi, LTE: no signal through rock
• Cable cut by falls, water, machines
• Voice and text do not show the face
• GPS does not locate a person in the heading
What is needed
• Video along the heading where there is line of sight
• An alert that survives a cut cable or a lost beam
• Dependable communication, as DGMS practice expects
Same problem as in last year’s presentation on underground mine communication.
Notes: This is the background from the earlier deck, stated plainly.
Present practice is leaky feeder and wired phones, plus low-rate radio. It is enough for voice on a drift that is still intact. It is not enough when the cable goes with the fall, and it never shows the face.
DGMS: do not promise certification in this grant. Say that dependable communication is part of mine safety practice, and that any statutory clearance will be taken before production deployment, as written in the proposal.
If asked what changed since the earlier presentation: the problem is the same. The system in the submitted proposal is the hybrid FSO–LoRa relay, built on the auto-tracking hardware already in the department. A handheld RFID device is not the deliverable of this grant.

## Slide 4
02 · PROBLEM STATEMENT AND RELEVANCE TO THE MINING SECTOR
Relevance to underground mining
What an underground heading needs, set against the systems available today.
Need in the mine
Cable / leaky feeder
Wi-Fi / LTE
LoRa only
FSO only
This proposal
Reach the surface
in an emergency
Until the cable
is cut
No signal
in rock
Yes, at low
data rate
Only with a clear
sightline
LoRa stays up
if the beam drops
Live picture
of the face
Not the design
of these systems
No usable
bandwidth
Too slow
for video
Yes, while
alignment holds
Yes. Alignment
is closed-loop
After vibration
or a fall
The cable often
fails as well
Link is lost
An alert can
still be sent
Beam is lost
Alert remains.
Beam is reacquired
Fit for an Indian
underground mine
Often imported,
mine-wide install
Not an
underground system
Used for sensors,
not for video
Mostly shown
in the laboratory
Indigenous node,
one hop at a time
Primary focus declared in the proposal: 4S Mining
Safe — a picture of the face, and an alert if that picture drops, before a team is sent in.
Smart — camera, IMU, both radios and the steering loop in one node.
Sustainable — heavy data on the optical link; control traffic on low-power radio.
Social — fewer people exposed to a heading the surface cannot see.
NIT Rourkela · FTBI–TEXMiN · Relevance to mining
4 / 14
Notes: Stay on the last column. Cable reaches the surface until it is cut. LoRa can carry the alert and cannot carry the video. FSO can carry the video and loses it when the mount moves. This proposal keeps both, on a hop the length of a straight stretch of tunnel.
Do not claim this replaces leaky feeder for voice across a whole mine. It is a heading kit: video on the clear spans, an alert that does not share the fate of the cable.
4S is the focus area ticked in the proposal. One clause each is enough.

## Slide 5
03 · INNOVATION AND UNIQUENESS
What is different in the proposed system
NIT Rourkela · FTBI–TEXMiN · Innovation
5 / 14
1
Hybrid FSO and LoRa
FSO carries video. LoRa carries control, alerts and backup.
2
Multi-hop along the tunnel
A node every 50–100 m on line of sight. Longer heading means more relays, not a stronger laser.
3
IMU auto-tracking
IMU drives a motorized mount and corrects pointing. Prototype exists in the department.
4
Video as safety
A live view of the zone a team is about to enter.
5
One cyber-physical node
Senses (camera, IMU, gas, temperature, humidity), communicates, and steers the beam.
Why FSO works underground
The beam runs down the open tunnel, not through rock.
Notes: Spend time on points 2 and 3. Those answer the objection that FSO cannot work underground.
Point 2: the link is along the open tunnel, 50 to 100 metres, then repeated. Point 3: the mount is part of the link, and the first version of it already runs in the department.
Point 1 is the architecture in the proposal figure. Point 4 is the mining use of the bandwidth. Point 5 is why the work belongs in a CPS centre.
Import, if there is time: mine communication systems of this class are largely bought from Germany, the USA and China. This is an indigenous design for the tunnel in front of us.

## Slide 6
04 · TECHNICAL FEASIBILITY AND METHODOLOGY
Proposed scheme
Figure from the submitted proposal. FSO transceivers 1 to n carry real-time video on auto-tracked hops of 50–100 m. Each node has the laser, the IMU, the motorized mount and a LoRa radio. LoRa carries control and alerts to the surface base station.
NIT Rourkela · FTBI–TEXMiN · Proposed scheme
6 / 14
Notes: Leave this figure up. Walk it left to right.
Each underground node has four parts: FSO laser, IMU, motorized alignment, LoRa. The optical beam between two nodes is the video path, 50 to 100 metres, steered by the IMU. The chain continues to transceiver n. The surface station receives the monitoring view and the LoRa alerts.
If a span is blocked or the beam walks off, the video on that span stops and the LoRa alert does not. The tracking loop then tries to reacquire.
Do not invent a bitrate or a latency. Those targets are fixed in the first three months, after the camera and the laser are selected.

## Slide 7
04 · TECHNICAL FEASIBILITY AND METHODOLOGY
Starting point: auto-tracking FSO already working
NIT Rourkela · FTBI–TEXMiN · Feasibility
7 / 14
Auto-tracking FSO prototype, department laboratory, NIT Rourkela. This unit will be used. Alignment is not started from scratch.
What this grant adds
+
Video on the optical hop
+
LoRa for alerts and fallback
+
Relay nodes along a heading
+
Surface station and underground enclosure
Why the rest can be built here
50–100 m
line-of-sight hop is within ordinary laser and photodiode modules
Lab ready
FSO transceivers, embedded benches, computing
Designed loss
if the beam drops, the alert goes on LoRa
Notes: Show the photograph. Say clearly: this is a working auto-tracking FSO system in the department, and the project will use it.
Do not quote a range or an accuracy for this unit unless you have the measured number in front of you. The design target for the mine hop, 50 to 100 metres, is the proposal target, not a result already claimed for this bench unit.
Then the four additions: video, LoRa, relays, underground enclosure and trial. The feasibility points are physics and facilities, not adjectives.

## Slide 8
04 · TECHNICAL FEASIBILITY AND METHODOLOGY
Work plan — 24 months
Schedule as given in the proposal. Every package is led by the PI, with two project assistants.
Months
Work
Milestone in the proposal
1–3
Select and procure FSO modules, IMUs, LoRa, cameras and the mount hardware
Month 3 — hardware procured
4–8
Architecture and the communication framework
Month 7 — architecture finalised; design package closes month 8
8–11
Auto-tracking on the mine node, using the existing department prototype
Month 11 — tracking ready
12–16
Integrate transmitter, relay nodes and the surface base station
Month 16 — prototype integrated
17–19
Laboratory tests: link stability, alignment, video quality, latency
Month 19 — laboratory validation
20–22
Test in a tunnel-like or underground environment; record reliability, tracking and energy
Month 22 — field validation
23–24
Documentation, deployment guidelines, patent filing, commercialization plan
Month 24 — report and filing
NIT Rourkela · FTBI–TEXMiN · Work plan
8 / 14
Notes: Do not read every row. Give the gates: month 3 hardware, month 7 architecture, month 11 tracker, month 16 integrated prototype, month 19 laboratory, month 22 tunnel-like test, month 24 patent and commercialization plan.
Point at months 8 to 11 and say that this block adapts the prototype already running in the department. The dates in the proposal are unchanged.
The tunnel trial does not start unless the month 16 and month 19 results justify it. If the optical hop drops during the trial, LoRa is the path under test for the alert.

## Slide 9
05 · EXPECTED OUTCOMES AND TECHNOLOGY READINESS LEVEL
Outcomes and readiness
NIT Rourkela · FTBI–TEXMiN · Outcomes and TRL
9 / 14
Readiness
TRL 1
TRL 2
TRL 3
TRL 4
TRL 5
TRL 6
TRL 7
TRL 8
TRL 9
Today
integrated system
Month 24
tunnel-like test
After this grant
needs a test mine
Deliverables
1
Hybrid FSO–LoRa prototype: transmitter, relays, surface base station
2
Real-time video over more than one optical hop
3
Auto-tracking recovering from deliberate misalignment
4
LoRa alert delivered when a hop is interrupted
5
Validation report, deployment guidelines, commercialization plan, patent filing
Notes: Be exact on the numbers. Do not raise the integrated system above TRL 2. The proposal says TRL 2. What is ahead of that is the auto-tracking prototype, which is a subsystem, not the whole mine link.
Month 24 commitment is TRL 5: relevant environment, meaning tunnel-like or underground, not only the optical bench. TRL 6 needs a partner or TEXMiN site and is outside this budget.
If they ask for numbers we will measure, and not for numbers we already have: hop length against 50–100 m, video continuity, time to realign, whether the alert arrives when the beam is blocked, and energy per node. Latency and bitrate are set in months 1 to 3.

## Slide 10
06 · INDUSTRY READINESS AND COLLABORATION
Industry engagement
NIT Rourkela · FTBI–TEXMiN · Industry
10 / 14
No industry letter is attached. It is to be earned from an operator or manufacturer who has seen a supervised trial.
1
Months 1–6
Find partners
Identify an underground operator and a mine-communications maker with TEXMiN and the industry cell. Ask for a letter of interest.
2
Months 6–12
Workshop
Their engineer on mounting, power, dust, gas zones. Constraints frozen before the enclosure closes.
3
Months 18–22
Trial
TEXMiN test mine or partner drift, engineer present. Report video, realignment, alert delivery.
4
Months 22–24
Next step
Licence or pilot talk. FTBI incubation if it becomes a venture.
Users
Underground coal and metal mines (managers, safety officers, rescue rooms) and mine-communication equipment makers.
Asked of TEXMiN, non-financial
Mentorship on mining standards, commercialization guidance, and test-mine access if it can be arranged.
Notes: Say the first sentence before anyone asks. A letter is not in the file.
Do not name Coal India or any other company as a partner. They are the class of user.
The useful introduction from the committee is a safety or communications engineer who will spend time on constraints in months 6 to 12, before the mechanical design is frozen.
Regulatory clearance is taken before product deployment, as the proposal states, not before the laboratory work.

## Slide 11
07 · IMPACT AND COMMERCIALIZATION PLAN
Impact, and how it would be deployed
NIT Rourkela · FTBI–TEXMiN · Impact and commercialization
11 / 14
What the tunnel trial will measure
Video continuity
on a 50–100 m hop
Alert delivery
when the hop is interrupted
Realignment time
after a deliberate disturbance
Energy per node
and bill of materials
What it changes for a mine
1
Re-entry decisions taken with a current picture of the face
2
The alert does not depend on a single cable
3
An indigenous node, where this class is largely imported
Commercial path
This grant
Proves one heading
Pilot
Supervised, with the partner who signs the letter
Licence or FTBI
Manufacturer licence, or incubated venture
Scale
Coverage grows by adding hops
Notes: The left side of the argument is the four measurements. Read one of them: when the beam is blocked, does the alert still arrive?
Do not quote lives saved, downtime percentages or rupees. We do not have those figures. The trial is how they would be obtained.
Commercial unit is a heading: node, relays, surface station. That is why a 15 lakh prototype is a step toward a product.
Later extensions, only if asked: video analytics, gas-trend monitoring, robotic nodes. They are in the proposal as future work. They are not month-24 deliverables.

## Slide 12
08 · TEAM DETAILS AND BUDGET SUMMARY
Team
NIT Rourkela · FTBI–TEXMiN · Team
12 / 14
Principal Investigator
Prof. Sadananda Behera
Assistant Professor
NIT Rourkela
98610 77539
No co-PI. Two project assistants for 24 months. The PI leads every work package.
Relevant experience
JLT, JOCN
Optical links under impairment: soft-failure detection and localization
Indian patent
Published application for a deployable hardware testbed
2 DoT / TCoE projects
Co-PI on 6G projects, about ₹80 lakh and ₹82.4 lakh. One is a hybrid transceiver
Division of the work
Project assistant 1
Hardware: FSO, IMU, pan-tilt, LoRa, PCB, enclosure
₹15,000 / month
Project assistant 2
Software: multi-hop forwarding, video, tracking loop, surface display
₹15,000 / month
Notes: One line of credibility: the PI’s work is optical links under impairment, and hardware that leaves the simulator. This project points that at a mine heading.
Do not read the publication list. If asked: JLT and JOCN; Indian patent application 202631017889, published 2026; two ongoing DoT projects, of which the hybrid transceiver is the closest.
The question to expect: there is no mining co-PI. Answer from the third bullet. Mining constraints enter through TEXMiN and the industry workshop. This group builds the link.

## Slide 13
08 · TEAM DETAILS AND BUDGET SUMMARY
Budget — ₹15.00 lakh
Figures in ₹ lakh, as submitted. Institute overhead is zero. Year 1 is ₹7.60 lakh. Year 2 is ₹7.40 lakh.
Head
Year 1
Year 2
Total
Share
Use
Two project assistants
3.60
3.60
7.20
48%
Hardware and software for 24 months
Equipment
2.00
1.50
3.50
23%
FSO, tracking, LoRa, cameras, power, enclosures
Consumables
0.75
0.75
1.50
10%
PCBs, mounts, cables, cells, small parts
Contingency
0.75
0.75
1.50
10%
Spares and prototype iterations
Travel
0.50
0.80
1.30
9%
Tunnel trials, partner visits, reviews
Overhead
0
0
0
0%
Waived
Total
7.60
7.40
15.00
100%
Year-1 equipment is the link: FSO modules, pan-tilt, IMUs, controllers, cameras, LoRa and gateway, batteries, enclosures, edge computer, lenses and mounts. Year-2 equipment is antennas, PCB fabrication and a 3D printer for mounts. The line-item list is in the proposal.
NIT Rourkela · FTBI–TEXMiN · Budget
13 / 14
Notes: One sentence: fifteen lakh, no overhead, two people and the hardware for one heading.
The columns add up: 7.20 + 3.50 + 1.50 + 1.50 + 1.30 = 15.00. Year split 7.60 and 7.40.
Salary is the largest head because the work is a build. Two assistants at 15,000 rupees a month for 24 months is 7.20 lakh. Equipment stays at 3.50 lakh because the unit under test is a heading, not a mine-wide installation. Travel is higher in year 2 because that is the tunnel trial.
Gas, temperature and humidity sensors are in the proposal justification and sit inside the hardware and consumables.

## Slide 14
FTBI–TEXMiN MINING CPS CoE
Thank you.
Request: ₹15 lakh over 24 months, to take the department’s auto-tracking
FSO prototype to a hybrid underground link, validated at TRL 5.
Prof. Sadananda Behera
Assistant Professor, National Institute of Technology Rourkela
98610 77539
NIT Rourkela · FTBI–TEXMiN · Close
14 / 14
Notes: Read the request once and stop. Invite questions.
Answers to keep short:
Letter — not in the file. Months 1–6 find the counterpart, 6–12 learn their heading, 18–22 trial with them present.
Why FSO underground — the beam crosses open tunnel, 50–100 m, not rock. Relays follow the heading. The IMU mount exists because a fixed bracket will not hold, and a version of it already runs in the department.
Leaky feeder — remains useful for voice on an equipped drift. This work adds a picture and an alert path on one heading.
TRL — integrated system is TRL 2. Auto-tracking prototype is already working. Target is TRL 5. TRL 6 needs a partner site.
No mining co-PI — TEXMiN mentors and the month-6 workshop. The enclosure is not frozen before that.
Audio — the new capacity is live video. LoRa carries alerts and control.
Laser safety — power, enclosure and exposure are part of the month-6 constraints. Clearance before any production deployment.