## Slide 1
TECHNOLOGY DEVELOPMENT PROPOSAL · FTBI–TEXMiN MINING CPS CoE
Underground Audio/Video
Communication System
for Miner Safety
and Monitoring
Hybrid free-space optical and LoRa communication for real-time video and emergency alerts in underground mines.
Underground nodes · 50–100 m hops
Focus
4S Mining
Safe, Smart, Sustainable, Social
Funding
₹15 lakh
24 months
Readiness
TRL 2 → TRL 5
Tunnel-level validation
Institute
NIT Rourkela
Prof. Sadananda Behera, PI
Prof. Sadananda Behera, Assistant Professor · 98610 77539 · No co-PI · Industry letter: not attached
NIT Rourkela · FTBI–TEXMiN · Title
1 / 15
Notes: Introduce the project in one line: a hybrid link that carries live video on free-space optics and keeps an alert path on LoRa for underground mines. The ask is ₹15 lakh for 24 months, taking the work from TRL 2 to TRL 5. An industry letter is not attached; the plan for getting one is on slide 11. An auto-tracking FSO prototype already exists in the department and is the starting point.

## Slide 2
01 · PROJECT TITLE AND OBJECTIVES
Objective
NIT Rourkela · FTBI–TEXMiN · Objectives
2 / 15
Real-time video from a mine heading to the surface on aligned free-space optical hops, with LoRa keeping the alert path alive.
Specific objectives
1
50–100 m
Real-time video on FSO links between successive tunnel nodes
2
IMU
Auto-tracking with motorized steering. Department prototype already working
3
LoRa
Control, alerts and fallback when an optical hop is interrupted
4
Multi-hop
Transmitter, relays, surface base station. Lab and tunnel-like tests
Notes: Read the objective once, then the four boxes. The existing auto-tracking prototype is the base for the second objective. The last box is the limit of this grant: a lab prototype and a test in a tunnel-like or underground setting. A trial in a working mine comes after that.

## Slide 3
02 · PROBLEM STATEMENT AND RELEVANCE TO THE MINING SECTOR
Background: communication underground today
NIT Rourkela · FTBI–TEXMiN · Background and problem
3 / 15
Miners at the face depend on a link that rock, water and ground movement regularly remove.
Surface control room
✕
Wi-Fi, LTE: no signal in rock
Cable cut by fall, water, machines
Voice and text do not show the face
What mines use now
Wired phones
Leaky-feeder cable
Low-rate radio
Surface control room
Need: video where there is line of sight, and an alert that survives a cut cable.
Notes: Mines today use wired phones, leaky-feeder cable and low-rate radio. These are fine for voice on an intact drift. When a fall or water cuts the cable, the link goes with it, and none of them shows the face. Wi-Fi and LTE do not pass through rock. So the need is a link that carries video where there is line of sight and still sends an alert when the cable or the beam is lost.

## Slide 4
02 · PROBLEM STATEMENT AND RELEVANCE TO THE MINING SECTOR
Relevance to underground mining
NIT Rourkela · FTBI–TEXMiN · Relevance to mining
4 / 15
What an underground heading needs, set against the systems available today.
Cable / leaky feeder
Wi-Fi / LTE
LoRa only
FSO only
This proposal
Reach the surface in an emergency
~
Until the cable is cut
✕
No signal in rock
✓
Yes, at low data rate
~
Only with clear sightline
✓
LoRa stays up if beam drops
Live picture of the face
✕
Not what it is for
✕
No usable bandwidth
✕
Too slow for video
✓
Yes, while aligned
✓
Aligned by closed loop
After vibration or a fall
✕
Cable often fails too
✕
Link lost
✓
Alert can still be sent
✕
Beam is lost
✓
Alert stays. Beam reacquired
Fit for an Indian underground mine
~
Often imported
✕
Not an underground system
~
Sensors, not video
~
Mostly shown in lab
✓
Indigenous node
Works
Partly
Does not
Safe
Picture of the face, alert if it drops
Smart
Camera, IMU, radios and steering in one node
Sustainable
Heavy data on light, control on low-power radio
Social
Fewer people sent into a heading unseen
Notes: Go down the last column. A cable reaches the surface until it is cut. LoRa can carry an alert but not video. FSO can carry video but loses it when the beam moves. This proposal combines the two and keeps the beam aligned with a feedback loop. It is a system for one heading, not a replacement for voice across the whole mine. The focus area is 4S Mining, shown in the four tiles at the bottom.

## Slide 5
03 · INNOVATION AND UNIQUENESS
What is different in the proposed system
NIT Rourkela · FTBI–TEXMiN · Innovation
5 / 15
1
Hybrid FSO and LoRa
FSO carries video. LoRa carries control, alerts and backup.
2
Multi-hop along the tunnel
A node every 50–100 m on line of sight. A longer heading needs more relays.
3
IMU auto-tracking
IMU drives a motorized mount and corrects pointing. Prototype exists in the department.
4
Video as safety
A live view of the zone a team is about to enter.
5
One cyber-physical node
Senses (camera, IMU, gas, temperature, humidity), communicates, and steers the beam.
Why FSO works underground
Beam follows the open tunnel
Notes: Spend time on cards 2 and 3. They answer the usual question of how free-space optics can work underground: the beam runs along the open tunnel for 50 to 100 m and the next node picks it up. The IMU mount deals with misalignment, and a first version already runs in the department. Cards 1, 4 and 5 are the hybrid architecture, video as a safety tool, and the cyber-physical design.

## Slide 6
04 · TECHNICAL FEASIBILITY AND METHODOLOGY
Proposed scheme
NIT Rourkela · FTBI–TEXMiN · Proposed scheme
6 / 15
FSO
Video on auto-tracked hops of 50–100 m.
IMU
Holds the beam on the next node.
LoRa
Control and alerts to the surface.
FSO beam: real-time video
LoRa link: control, alerts
Each node: laser, IMU, motorized mount, LoRa. Surface: dashboard, alerts, localization.
Notes: This is Fig. 1 from the proposal. Walk through it from left to right. Each underground node has a laser, an IMU, a motorized alignment mount and a LoRa module. The orange beam between nodes carries the video, 50 to 100 m per hop. The dotted LoRa link carries control signals and alerts to the surface base station. If a hop is blocked, the video on that hop stops but the alert still arrives. Bit rate and latency targets will be fixed in the first three months, once the camera and laser are chosen.

## Slide 7
04 · TECHNICAL FEASIBILITY AND METHODOLOGY
How one hop works
NIT Rourkela · FTBI–TEXMiN · How one hop works
7 / 15
The picture travels as light. Each node rebuilds it, checks it and sends it on.
Optical frame
AA55
Length
Seq
JPEG
CRC-16
UART 115200 8N1, one direction
Camera node
• Camera + Raspberry Pi
• Packet out of UART
• 650 nm laser, on–off keying
light
Relay node
• Photodiode, amplifier, comparator
• Second Pi checks CRC, holds JPEG
• Sends the frame again on its own laser
light
Base station
• Same receiver chain
• Third Pi checks CRC
• JPEG on the HDMI screen
Three different jobs
Laser
Carries the JPEG only.
IMU
Holds the camera head at its angle. It does not find the relay.
LoRa
Five bytes: lock or lost, alert, image OK. No JPEG.
Notes: The camera node packs one JPEG into a small frame: start mark, length, sequence number, the JPEG and a CRC. The Pi sends it over UART to a 650 nm laser that is switched on and off with the bits. At the relay, a photodiode, amplifier and comparator turn the light back into bits. A second Pi checks the CRC, keeps the JPEG and sends the same frame out on its own laser. The relay does not amplify the light; it rebuilds the picture. The base does the same and shows the JPEG on a screen. Three separate jobs: the laser carries the JPEG, the IMU holds the camera head at its angle, and LoRa sends five-byte messages such as lock, lost and alert.

## Slide 8
04 · TECHNICAL FEASIBILITY AND METHODOLOGY
Starting point: auto-tracking FSO already working
NIT Rourkela · FTBI–TEXMiN · Feasibility
8 / 15
Auto-tracking FSO prototype in the department lab. This unit will be reused.
What this grant adds
+
Video on the optical hop
+
LoRa for alerts and fallback
+
Relay nodes along a heading
+
Surface station, underground enclosure
Why it can be built here
50–100 m
hop within ordinary laser and photodiode modules
In the lab
FSO transceivers, embedded benches, computing
Designed loss
beam drops, alert goes on LoRa
First milestone: laboratory bench, one relay
Relay laser hand-aimed. IMU loop off for the first JPEG.
Camera node
existing gimbal, camera, Pi, laser
Relay
the one new node
Base
receiver, Pi, HDMI screen
2–5 m
2–5 m
Notes: This is the working auto-tracking FSO unit in our laboratory. We will reuse it instead of starting alignment from scratch. The grant adds video, LoRa, relay nodes, a surface station and an enclosure for the underground trial. The first milestone is a bench setup: camera node, one new relay and a base, 2 to 5 m apart. The relay laser is aimed by hand and the IMU loop is off for the first JPEG. If the picture appears on the base screen, both hops work. Quote a range or accuracy for the existing unit only if we have the measured number.

## Slide 9
04 · TECHNICAL FEASIBILITY AND METHODOLOGY
Work plan: 24 months
NIT Rourkela · FTBI–TEXMiN · Work plan
9 / 15
Year 1
Year 2
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
1
Procure FSO, IMU, LoRa, cameras, mounts
2
Architecture and communication framework
3
Auto-tracking on the mine node
4
Integrate transmitter, relays, base
5
Laboratory tests
6
Tunnel-like / underground test
7
Documentation, patent, commercial plan
Milestones: M3 hardware · M7 architecture · M11 tracking · M16 integrated · M19 lab · M22 field · M24 report
Risk management
Technical
LoRa backup and modular hardware
Operational
Phased build with test checkpoints
Financial
Conservative budget margins
Notes: Give the gates rather than every row: month 3 hardware, month 7 architecture, month 11 tracking, month 16 integrated prototype, month 19 lab validation, month 22 tunnel-like test, month 24 report and patent filing. Point at row 3 (tracking reuses the existing prototype) and row 6 (the tunnel test depends on the lab results). The three risks at the bottom are from the proposal: LoRa backup with modular hardware, phased testing, and conservative budget margins.

## Slide 10
05 · EXPECTED OUTCOMES AND TECHNOLOGY READINESS LEVEL
Outcomes and readiness
NIT Rourkela · FTBI–TEXMiN · Outcomes and TRL
10 / 15
Readiness
TRL 1
TRL 2
TRL 3
TRL 4
TRL 5
TRL 6
TRL 7
TRL 8
TRL 9
Today
integrated system
Month 24
tunnel-like test
After this grant
needs a test mine
Deliverables
1
Hybrid FSO–LoRa prototype: transmitter, relays, surface base station
2
Real-time video over more than one optical hop
3
Auto-tracking recovering from deliberate misalignment
4
LoRa alert delivered when a hop is interrupted
5
Validation report, deployment guidelines, commercialization plan, patent filing
Notes: Keep the TRL numbers exact. The integrated system is at TRL 2 today. The auto-tracking unit is a working subsystem, not the whole link. The target at month 24 is TRL 5, a tunnel-like or underground test. TRL 6 needs a partner or TEXMiN test mine and is outside this grant. What we will measure: hop length against 50 to 100 m, video continuity, time to realign, whether the alert arrives when the beam is blocked, and energy per node.

## Slide 11
06 · INDUSTRY READINESS AND COLLABORATION
Industry engagement
NIT Rourkela · FTBI–TEXMiN · Industry
11 / 15
No industry letter is attached yet. We plan to get one after a supervised trial with an operator or manufacturer.
1
Months 1–6
Find partners
Identify an underground operator and a mine-communications maker with TEXMiN and the industry cell. Ask for a letter of interest.
2
Months 6–12
Workshop
Their engineer on mounting, power, dust, gas zones. Constraints frozen before the enclosure closes.
3
Months 18–22
Trial
TEXMiN test mine or partner drift, engineer present. Report video, realignment, alert delivery.
4
Months 22–24
Next step
Licence or pilot talk. FTBI incubation if it becomes a venture.
Users
Underground coal and metal mines (managers, safety officers, rescue rooms) and mine-communication equipment makers.
Asked of TEXMiN, non-financial
Mentorship on mining standards, commercialization guidance, and test-mine access if it can be arranged.
Notes: Say this first: an industry letter is not attached. The plan is to find an underground operator and a mine-communication maker in months 1 to 6, hold a workshop with their engineer in months 6 to 12 so that mounting, power, dust and gas-zone limits are known before the enclosure is frozen, and run the trial with them present in months 18 to 22. Avoid naming any company as a partner. From TEXMiN we ask for mentorship on standards, commercialization guidance and test-mine access if possible. Regulatory clearance is taken before any deployment.

## Slide 12
07 · IMPACT AND COMMERCIALIZATION PLAN
Impact, and how it would be deployed
NIT Rourkela · FTBI–TEXMiN · Impact and commercialization
12 / 15
What the tunnel trial will measure
Video continuity
on a 50–100 m hop
Alert delivery
when the hop is interrupted
Realignment time
after a deliberate disturbance
Energy per node
and bill of materials
What it changes for a mine
1
Re-entry decisions taken with a current picture of the face
2
The alert does not depend on a single cable
3
An indigenous node, where this class is largely imported
Commercial path
This grant
Proves one heading
Pilot
Supervised, with the partner who signs the letter
Licence or FTBI
Manufacturer licence, or incubated venture
Scale
Coverage grows by adding hops
Also fits
Tunnel monitoring
Underground transport
Oil and gas sites
Notes: The trial gives four measurements: video continuity, alert delivery when the hop is cut, time to realign, and energy per node. We do not yet have figures for lives saved, downtime or rupee savings, so none are quoted. The commercial path is this grant, a supervised pilot, a licence or FTBI incubation, and then growth by adding hops. Video analytics, gas-trend monitoring and drone or robot nodes are future work and are not part of the 24-month deliverables.

## Slide 13
08 · TEAM DETAILS AND BUDGET SUMMARY
Team
NIT Rourkela · FTBI–TEXMiN · Team
13 / 15
Principal Investigator
Prof. Sadananda Behera
Assistant Professor
NIT Rourkela
98610 77539
No co-PI. Two project assistants for 24 months. The PI leads every work package.
Mining practice comes from TEXMiN mentors and the industry engineer, before the enclosure is frozen.
Relevant experience
JLT, JOCN
Optical links under impairment: soft-failure detection and localization
Indian patent
Published application for a deployable hardware testbed
2 DoT / TCoE projects
Co-PI on 6G projects, about ₹80 lakh and ₹82.4 lakh. One is a hybrid transceiver
Division of the work
Project assistant 1
Hardware: FSO, IMU, pan-tilt, LoRa, PCB, enclosure
₹15,000 / month
Project assistant 2
Software: multi-hop forwarding, video, tracking loop, surface display
₹15,000 / month
Notes: One line on credibility: the PI works on optical links and hardware testbeds, with two ongoing DoT/TCoE 6G projects and a published Indian patent application. There is no mining co-PI. Mining practice will come from TEXMiN mentors and from the industry engineer in the month-6 workshop. Two project assistants: one for hardware, one for software.

## Slide 14
08 · TEAM DETAILS AND BUDGET SUMMARY
Budget: ₹15.00 lakh
NIT Rourkela · FTBI–TEXMiN · Budget
14 / 15
In ₹ lakh. Institute overhead is zero. Year 1 is ₹7.60 lakh and Year 2 is ₹7.40 lakh.
Chart: 
| Project assistants | Equipment | Consumables | Contingency | Travel
Budget | 7.2 | 3.5 | 1.5 | 1.5 | 1.3
₹15.00
lakh · 24 months
Head | Year 1 | Year 2 | Total | Share
Project assistants (2) | 3.60 | 3.60 | 7.20 | 48%
Equipment | 2.00 | 1.50 | 3.50 | 23%
Consumables | 0.75 | 0.75 | 1.50 | 10%
Contingency | 0.75 | 0.75 | 1.50 | 10%
Travel | 0.50 | 0.80 | 1.30 | 9%
Overhead | 0 | 0 | 0 | 0%
Total | 7.60 | 7.40 | 15.00 | 100%
Equipment
Year 1: FSO modules, pan-tilt, IMUs, controllers, cameras, LoRa and gateway, batteries, enclosures, edge computer, optics. Year 2: LoRa antennas, PCB fabrication, 3D printer for mounts.
Notes: Total ₹15 lakh with no institute overhead. Year 1 is 7.60 and year 2 is 7.40. The two project assistants are the largest head at 7.20 lakh, because this is a build project. Equipment is 3.50 lakh, consumables 1.50, contingency 1.50 and travel 1.30, which is higher in year 2 for the tunnel trials. Gas, temperature and humidity sensors are covered within equipment and consumables.

## Slide 15
FTBI–TEXMiN MINING CPS CoE
Thank you.
Request: ₹15 lakh over 24 months, to take the department’s auto-tracking FSO prototype to a hybrid underground link, validated at TRL 5.
Prof. Sadananda Behera
Assistant Professor, National Institute of Technology Rourkela
98610 77539
NIT Rourkela · FTBI–TEXMiN · Close
15 / 15
Notes: Read the request once and invite questions. Likely questions and short answers. Industry letter: not in the file; the plan is on slide 11. Why FSO underground: the beam runs down the open tunnel for 50 to 100 m and relays follow the heading. Leaky feeder: still useful for voice; this adds a picture and an alert path on one heading. TRL: the integrated system is TRL 2, the target is TRL 5, and TRL 6 needs a partner site. Laser safety: power, enclosure and exposure are part of the month-6 workshop, with clearance before any deployment. Audio: the new capacity is live video; LoRa carries alerts and control.